Installation

- Remove the diffuser from the base by rotating anti-clockwise.  Unscrew the three retaining screws and rotate the gear tray to remove.

- Carefully remove the knock-out (20mm cable entry and Besa mountings at centre of the base).

- Position and fix the base to a suitable solid surface using screws supplied, sealant should be applied around the screw heads to reduce water ingress if the luminaire is to be mounted externally (Luminaires should not be installed where the illuminated surface is within 0.5m from the front of the fitting). NOTE: If mounting on a BESA conduit box, a suitable gasket (rubber) should be used.

- Secure supply cable into the luminaire through cable entry ensuring that a cable gland, grommet or sealing compound is used to maintain the IP rating of the luminaire.

- Terminate the cable into the terminals ensuring correct polarity is observed.

- Please see below for electrical connections.

Electrical Connections

Connect as follows :-  	LIVE			(L)	BROWN OR RED	(switched)

NEUTRAL		(N)	BLUE OR BLACK

EARTH				GREEN & YELLOW

- Re-attach the gear tray back into position.

- Re-fit the diffuser, taking care to ensure it is properly seated.

- Restore power supply, switch on and test for satisfactory operation.

IP65